## Slide 1
TRACK · DIGITAL ASSET MANAGEMENT
PRANA
प्राण
India's electrochemical grid battery
PROCESS RESPONSE & ADAPTIVE NETWORK AGENT
The cell house is the battery. Its state of charge is the caustic tank, and no plant in India dispatches it.
Buddharatna Hingole
IIT Mandi
Platinum Jubilee Innovation Hackathon
MC²⁺ · Oil India Limited · IIT Kharagpur
01 · THE OPPORTUNITY
Power price within a single delivery day
Midday clears near ₹2/kWh while the evening peak runs to the ₹10 cap. A flat industrial load pays that spread every day.
02 · THE ASSET
Where the storage already sits
Four rectifier trains, one caustic tank. The tank is the state of charge: run the cells hard on cheap power, then coast through the evening on stored caustic. Tonnes shipped stay the same.
Notes: Open flat. Name, one line, then move. Left is who we are; right is the whole thesis in two pictures — the price signal that makes flexibility valuable, and the asset that already exists to supply it. The line to land: the cell house is the battery.

## Slide 2
MARKET EVIDENCE
02 / 10
Evening power now costs 3.5× midday power
IEX real-time market, Maharashtra W2 — mean evening price divided by mean solar-hour price, on every settled 15-minute block since April 2022.
EVENING-TO-MIDDAY PRICE RATIO, BY FINANCIAL YEAR
1.47
2022-23
1.46
2023-24
1.87
2024-25
2.23
2025-26
3.53
2026-27 *
21.1%
of the year now clears below ₹2/kWh, up from 4.1%
₹10/kWh
the regulatory cap, hit repeatedly in the evening peak
152,542
settled blocks behind these figures — nothing modelled
* April–August 2026 only — India's peak-demand and peak-solar months. Seasonally biased upward; it indicates acceleration, it does not measure it.
Notes: Settled money, not a forecast. 152,542 blocks. Say the FY2026-27 caveat out loud before anyone catches it: April to August only, India's peak-solar and peak-demand months, seasonally biased upward. It indicates acceleration; it does not measure it.

## Slide 3
THE CUSTOMER
03 / 10
For a chlor-alkali plant, electricity is the feedstock
Indian producers buy from the grid, own their cell house, and run a flat profile into a market that now moves 3.5× within the day.
CASH COST OF A TONNE OF CAUSTIC SODA
Power 55–70%
Salt, steam, labour, capital
A refinery would never take this meeting — power is a minor line for them, and they burn their own captive generation. Here it is the P&L.
1.34 GW
of rectifier load nationally — 6.0 MTPA capacity, 11.7 TWh a year
₹155 cr
a year of avoidable cost sector-wide, at our measured ₹0.133/kWh
Zero
capex, and zero change in tonnes shipped — by construction
Power share of production cost: National Productivity Council of India, Chlor-Alkali Sector Manual, p.22.
Notes: Chlor-alkali is the customer because power is the raw material. Grid-exposed, owns the asset, and the works manager already avoids peak hours by hand. We are asking them to do an existing behaviour optimally.

## Slide 4
THE INSIGHT
04 / 10
The cheapest storage in India is already built
THE CONSENSUS ANSWER
411 GWh
of grid batteries to be constructed by 2031-32, at ₹0.6–1.1 crore per MWh installed.
→
ALREADY IN THE TANK, ONE PLANT
748 MWh
21.8 MW deliverable, stored as caustic soda, dispatched by nobody. Displaces ₹450–820 crore of battery.
Quoted at the deliverable floor, not the safety floor. Chlorine is made stoichiometrically and cannot be stored in bulk, so the chlorine consumer's turndown — 70% of design — is the real limit, not the cell's 40% H₂-in-Cl₂ interlock. Quoting the interlock would have claimed 1,410 MWh, and half of that battery does not exist.
Notes: The consensus answer is to build 411 GWh. Fine — that build must happen. But one 700 TPD plant already holds 748 deliverable megawatt-hours, and nobody dispatches it. Stress the word deliverable: we quote the chlorine consumer's floor, not the cell's safety interlock.

## Slide 5
THE TWIN
05 / 10
The convexity is derived, not assumed
V = V₀ + k·i
cell voltage law
q ∝ i
Faraday's law
P(q) = αq + βq²
Convex, by electrochemistry rather than by parameter choice. Splitting production into a turn-down leg and a rebuild leg therefore always burns more kilowatt-hours than running steady — even though the tonnes are identical. That excess is the true physical cost of flexibility.
SPECIFIC ENERGY FALLS ON TURN-DOWN
E = 2.41 + 0.329·i + 0.24·log i
The NPC's published empirical cell equation gives a plant that is more efficient per tonne as it turns down. This is the one industrial process paid, in energy terms, to be flexible.
WE CHARGE OURSELVES THE LARGER LOSS
The published cell curve implies a β of 0.30–0.45 over the operating range. This model uses 0.21 , so every saving we report is understated rather than flattered.
NPC India, Chlor-Alkali Sector Manual, p.28 (voltage law) and p.29 (empirical cell curve). Linearised for the MILP by 16 tangent hyperplanes; measured error 0.025%.
Notes: This is the technical high point. I did not assume the convexity — electrochemistry gives it to me. Voltage rises linearly with current density, Faraday's law makes production proportional to current, so power is necessarily quadratic in production. And the Government of India's own published cell equation says specific energy FALLS on turn-down. Chlor-alkali is the one industrial process paid, in energy terms, to be flexible.

## Slide 6
THE PRODUCT
06 / 10
The flexibility cost curve no plant has for itself
φ(ΔMW, Δt)
The rupees per MWh it costs this plant to shed ΔMW for Δt hours, with product output held constant.
₹27–117
PER MWH SHIFTED, THIS CELL HOUSE
It is allowed to end
φ returns infinity where the flexibility does not exist. A curve that were finite everywhere would be promising megawatts the plant cannot deliver.
It carries the costs models omit
Membrane life consumed per unit of setpoint movement, chlorine diverted to the bleach plant, and the extra kVAh from power-factor droop on turn-down.
It is what nobody can write down
The constraints live in the interlock list, the HAZOP minutes and the board operator's head. An LLM agent elicits them; a human signs them off.
Notes: This is the novel object. Ask any Indian plant how many MW it can move, for how long, at what cost — no document answers. φ is that document. The number the plant has never had about itself.

## Slide 7
SYSTEM
07 / 10
Data to setpoint, in five stages that already run
01 · DATA
Settled market panel
152,542 IEX blocks, 1,588 complete days. MERC Case 75 of 2025, post-remand, read from the primary order.
→
02 · TWIN
Cell-house physics
Convex power curve, caustic tank as state of charge, chlorine balance, H₂-in-Cl₂ as a hard bound. Emits φ.
→
03 · FORECAST
Quantile price fan
LightGBM q10/q50/q90, conformally widened out of sample. MAE 1,072 against three baselines.
→
04 · DECISION
Stochastic MILP
96 blocks against landed cost, CVaR₉₅ risk term, demand charge inside the objective. CBC, 0.3 s.
→
05 · AGENT
Constraints and reasons
Elicits constraints from SOPs and operator speech, gated on human sign-off. Explains from the solver, not from itself.
~3,000 lines of Python, 45 regression tests passing, and every schedule re-simulated against the true nonlinear physics before anyone sees it.
Notes: One diagram, ten seconds each. The load-bearing detail is at the end: explanations come from the solver's binding constraints, not from the language model. It cannot invent a reason because it is never asked to produce one.

## Slide 8
RESULT
08 / 10
Optimising on the exchange price leaves money on the table
The market clearing price is about 60% of what an industrial consumer pays. Wheeling, surcharges, duty and the demand charge on peak kVA are the other 46% of the bill — so we put them inside the optimisation rather than after it.
SAME FIVE HIGH-SPREAD DAYS
OPTIMISED ON MCP
OPTIMISED ON LANDED COST
PENALTY
INDICATIVE PER YEAR
Chlor-alkali, 700 TPD
₹7.196 cr
₹7.128 cr
0.95%
₹5.0 cr
Refinery utilities block
₹9.167 cr
₹8.862 cr
3.33%
₹22.3 cr
Both schedules settled at the same real bill. The percentage is the robust figure; the annualisation is indicative.
The regulator is pushing the same way. MERC's post-remand order removes the night rebate because it competes with shifting load into solar hours, and the demand charge rises 15% over four years while the energy charge falls 12%. Flexibility gets more valuable on the published trajectory, not less.
Notes: Two schedules for the same days: one built against the exchange clearing price, one against the landed bill, both settled at the landed bill. Note we killed our own earlier version of this test — zeroing the demand charge leaves the peak variable unpriced, so the difference was degeneracy, not behaviour. Measuring the rupee penalty on a commonly-settled bill is the correct experiment.

## Slide 9
PROOF
09 / 10
120 consecutive days, replayed at settled prices
₹0.133
saved per kWh of total plant load, with real forecast error
₹9.17 cr
annualised · 1.53% of the bill
0
violations · 0 MW deviation used
13 / 120
days worse than doing nothing
FROM GROSS TO NET, ₹ LAKH OVER 120 DAYS
378.3
Electricity avoided, gross
−76.8
Membrane wear, chlorine dumped, kVAh droop
301.5
Net saving
One fifth of the gross is paid straight back to the plant. A model that does not charge these is not conservative — it is wrong.
120 delivery days to 2026-08-06, settled at realised prices. Counterfactual is one steady setpoint per asset held all day — how the plant is actually run. Perfect foresight would be ₹0.174/kWh; the forecast-error haircut is 22%.
Notes: Quote the forecast-error row, never perfect foresight. Everything is net: one fifth of the gross saving is paid straight back to the plant for membrane wear, dumped chlorine and kVAh droop. Thirteen bad days out of 120 — reported, not removed. A single-asset site with a hard 70% floor has no second lever when the forecast is wrong, which is the honest argument for adding a second flexible asset.

## Slide 10
OIL INDIA, AND THE ASK
10 / 10
The same machine Oil India is already building
Jorhat
The green hydrogen plant is electrochemically the same cell house. The twin already models it as a second archetype.
NRL
On this panel the LCOH minimum sits near 6,000 operating hours, not 8,000. A DPR written at 90% CUF is mis-sizing the plant.
57 GW by 2030
Every electrolyser the Green Hydrogen Mission builds is a grid battery nobody is currently planning to dispatch.
THE ASK
One chlor-alkali plant. Ninety days. Advisory only.
Weeks 1–4: fit the twin to their historian and deliver φ — the number they have never had about their own plant. Weeks 5–12: shadow mode, a recommended profile each morning, compared against actuals each evening at realised prices.
Success agreed up front: a 3% cut in landed power cost against their own actuals, zero product-spec excursions, zero approaches to the H₂-in-Cl₂ limit.
Cost to them: zero. Twenty per cent of verified savings if it works.
Notes: Close the loop explicitly. An electrolyser is a chlor-alkali cell with a different membrane — same voltage law, same convex curve, same twin, already implemented. Then the ask, and stop talking: one plant, 90 days, advisory only, costs them nothing.