## Slide 1
TRACK · DIGITAL ASSET MANAGEMENT
PRANA
प्राण
INDUSTRIAL FLEXIBILITY INTELLIGENCE
How much electrical flexibility can an industrial plant safely afford to use?
Turning process physics into safe, economic electricity decisions with the production objective untouched.
Buddharatna Hingole
IIT Mandi
Platinum Jubilee Innovation Hackathon
MC²⁺ · Oil India Limited · IIT Kharagpur
THE MARKET MOVES
Power price within one delivery day
THE PLANT DOES NOT
Load, inside the safe operating envelope
PROCESS RESPONSE & ADAPTIVE NETWORK AGENT

## Slide 2
THE MARKET PROBLEM
02 / 10
Electricity is no longer a flat-cost input
IEX real-time market, Maharashtra W2 mean evening price divided by mean solar-hour price, on every settled 15-minute block since April 2022.
EVENING-TO-MIDDAY PRICE RATIO, BY FINANCIAL YEAR
1.47
2022-23
1.46
2023-24
1.87
2024-25
2.23
2025-26
3.53
2026-27 *
21.1%
of the year now clears below ₹2/kWh, up from 4.1%
₹10/kWh
the regulatory cap, hit repeatedly in the evening peak
152,542
settled blocks behind these figures nothing modelled
Price volatility creates an economic opportunity — but only if plant flexibility can be quantified safely.
* April–August 2026 only India's peak-demand and peak-solar months. Seasonally biased upward; it indicates acceleration, it does not measure it.

## Slide 3
THE INDUSTRIAL PROBLEM
03 / 10
A plant cannot simply follow the electricity price
THE MARKET ASKS FOR
Low price
→ consume more
High price
→ consume less
Two rules, both of them ignorant of what the plant is making.
THE PLANT ANSWERS TO
Safety
Production
Quality
Inventory
Ramp rate
Equipment limits
Downstream demand
Electricity cost ranks below every one of these and always will.
THE FLEXIBILITY GAP
Electricity markets know the price. Plants know their process. The missing layer is the decision between them.
PRANA is that layer. It quantifies how much electrical flexibility a process can safely and economically use, and returns one of three answers each morning:
SHIFT
HOLD
DO NOTHING
DO NOTHING is a valid, frequent and important result.
A price signal alone is not an operating instruction. The same ₹/kWh can produce completely different decisions depending on what the plant is making, where it is operating, and which constraint is binding. PRANA converts that process context into an actionable energy decision.

## Slide 4
THE GENERAL SOLUTION
04 / 10
PRANA discovers flexibility it does not assume it
Potential flexibility sources plant-specific validation required. None of these is assumed flexible until its own physics says so.
Refinery
Compressors, utilities, intermediate tankage as a process buffer.
CANDIDATE
Chemicals
Batch scheduling freedom and intermediate inventory between units.
CANDIDATE
Fertilizer
Utilities, electrolysis where present, ammonia and urea buffers.
CANDIDATE
Chlor-alkali
Rectifier load, caustic inventory, chlorine offtake as the binding downstream constraint.
DEMONSTRATED · 120 DAYS
Hydrogen
Electrolyser operating envelope and downstream storage pressure.
CANDIDATE
The physics changes from industry to industry. The flexibility-intelligence framework remains the same.
Where the storage already sits
Four rectifier trains, one caustic tank. The tank is the state of charge: run the cells hard on cheap power, then coast through the evening on stored caustic. Tonnes shipped stay the same.
Notes: Read the label out loud: potential flexibility sources, plant-specific validation required. I am not claiming your compressor house is flexible — I am claiming nobody has measured whether it is. The physics changes from industry to industry; the framework does not. Q: What if the plant has no flexibility? Then φ comes back infinite across the useful range and PRANA says so in week four, before anyone has spent money on a deployment. That is a legitimate and cheap outcome. Q: Why does chlor-alkali prove a generalised concept? It does not prove the numbers generalise. It proves the method works end to end on one hard, safety-critical process — convex load physics, an inventory buffer, a downstream constraint and a hard interlock. A refinery has the same four ingredients with different equations.

## Slide 5
THE ENGINEERING CORE
05 / 10
From process physics to flexibility
PRANA uses a plant-specific physics model. Chlor-alkali is our demonstrated implementation — the equations below are its, not everyone's.
DERIVED, NOT FITTED
V = V₀ + k·i
cell voltage law
q ∝ i
Faraday's law
P(q) = αq + βq²
Convex by electrochemistry, not by parameter choice. Splitting output into a turn-down leg and a rebuild leg therefore always burns more kWh than steady operation that excess is the true physical cost of flexibility.
The published cell curve implies β of 0.30–0.45; this model uses 0.21, so we charge ourselves the larger round-trip loss.
Process physics
Convex load curve, energy per tonne, power factor
↓
Operating envelope
Hard interlocks and equipment limits as bounds
↓
Production & downstream
Tonnes committed, offtake that cannot be stored
↓
Inventory & ramp limits
Buffer capacity, rate of change the plant tolerates
↓
Flexibility cost φ
₹/MWh to move load, output held constant
NPC India, Chlor-Alkali Sector Manual, p.28 (voltage law) and p.29 (empirical cell curve, E = 2.41 + 0.329·i + 0.24·log i). Linearised for the MILP by 16 tangent hyperplanes; measured error 0.025%.
Notes: This slide is for the chemical and mechanical engineers. The point to make: the convexity is derived, not fitted. Voltage rises linearly with current density, Faraday's law makes production proportional to current, so power is necessarily quadratic in production — that is electrochemistry, not a regression. And the Government of India's own published cell equation says specific energy falls on turn-down. Then be explicit about scope: this is a plant-specific physics model, and chlor-alkali is our demonstrated implementation. A refinery model would carry compressor maps and tank levels instead. Q: How are process constraints determined? From the interlock list, the HAZOP minutes, the SOPs and the board operator — elicited by an agent, then signed off by a human engineer before it can bind. Q: How do you prevent AI from overriding safety? The language model never touches the setpoint. It only proposes constraints; the solver enforces them as hard bounds, and every schedule is re-simulated against the true nonlinear physics before a human sees it.

## Slide 6
THE NOVEL OBJECT
06 / 10
PRANA gives the plant a number it didn't have
φ(ΔMW, Δt)
The cost to this process of shifting electrical load by ΔMW for Δt hours, while respecting every production and engineering constraint.
LOW COST
Usable flexibility
The process can absorb the movement for less than the market pays for it. Recommend SHIFT.
HIGH COST
Probably uneconomic
Membrane wear, diverted product and reactive-power penalties eat the spread. Recommend HOLD.
INFINITE · UNAVAILABLE
Do not touch
The flexibility does not exist at that depth or duration. φ returns infinity rather than a number. DO NOTHING.
WHERE THE VIRTUAL BATTERY FITS
Quantify safe flexibility
→
Represent as power × duration
The virtual battery is a representation of measured flexibility never the purpose of the plant. We do not assume a process is a battery; we find what it can spare, then describe it in grid units.
PRANA does not ask “how much load can we shed?” It asks “how much flexibility can we safely afford?”
Notes: This is the novel object, and the slide to slow down on. Ask any plant in India how many megawatts it can move, for how long, at what cost to the process — no document answers. φ is that document. Read the hero line exactly: PRANA does not ask how much load can we shed, it asks how much flexibility can we safely afford. Then the virtual-battery point, carefully: we do not assume the process is a battery. We quantify its safe flexibility first; once quantified, that flexibility can be represented as a power-duration abstraction — a virtual battery. The abstraction is a representation of measured flexibility, never the purpose of the plant. Q: What if electricity savings are lower than process costs? φ already contains the process costs, so that case shows up as a high or infinite value and the answer is DO NOTHING.

## Slide 7
SYSTEM
07 / 10
Data to setpoint, in five stages that already run
01 · DATA
Settled market panel
152,542 IEX blocks, 1,588 complete days. MERC Case 75 of 2025, post-remand, read from the primary order.
→
02 · TWIN
Cell-house physics
Convex power curve, caustic tank as state of charge, chlorine balance, H₂-in-Cl₂ as a hard bound. Emits φ.
→
03 · FORECAST
Quantile price fan
LightGBM q10/q50/q90, conformally widened out of sample. MAE 1,072 against three baselines.
→
04 · DECISION
Stochastic MILP
96 blocks against landed cost, CVaR₉₅ risk term, demand charge inside the objective. CBC, 0.3 s.
→
05 · AGENT
Constraints and reasons
Elicits constraints from SOPs and operator speech, gated on human sign-off. Explains from the solver, not from itself.
~3,000 lines of Python, 45 regression tests passing, and every schedule re-simulated against the true nonlinear physics before anyone sees it.
Notes: One diagram, ten seconds each. The load-bearing detail is at the end: explanations come from the solver's binding constraints, not from the language model. It cannot invent a reason because it is never asked to produce one.

## Slide 8
ECONOMIC INTELLIGENCE
08 / 10
The plant doesn't pay MCP - it pays the landed bill
Market price
+
Wheeling
+
Surcharges
+
Duty
+
Demand charge on peak kVA
=
Landed cost
SAME FIVE HIGH-SPREAD DAYS
OPTIMISED ON MCP
OPTIMISED ON LANDED COST
Chlor-alkali, 700 TPD
₹7.196 cr
₹7.128 cr
Refinery utilities block
₹9.167 cr
₹8.862 cr
Both schedules settled at the same real bill. Same physics, same days — only the price the optimiser was shown differs.
PRANA optimises against the cost the plant actually pays.
The market clearing price is about 60% of what an industrial consumer pays. Wheeling, surcharges, duty and the demand charge on peak kVA are the other 46% of the bill so we put them inside the optimisation rather than after it.
The regulator is pushing the same way. MERC's post-remand order removes the night rebate because it competes with shifting load into solar hours, and the demand charge rises 15% over four years while the energy charge falls 12%. Flexibility gets more valuable on the published trajectory, not less.
PENALTY
INDICATIVE PER YEAR
0.95%
₹5.0 cr
3.33%
₹22.3 cr
Notes: An industrial consumer does not pay the exchange clearing price — that is roughly 60% of the bill. Wheeling, surcharges, duty and the demand charge on peak kVA are the rest, and the demand charge in particular punishes exactly the behaviour a naive optimiser produces: a deep, sharp peak. So we put the whole landed bill inside the objective rather than checking it afterwards. Both schedules on this slide are settled at the same real bill; the percentage is the robust number and the annualisation is indicative. Worth adding: MERC's post-remand order removes the night rebate and raises the demand charge 15% over four years while the energy charge falls 12% — the regulator is pushing the same way we are.

## Slide 9
PROOF · CASE STUDY
09 / 10
DEMONSTRATOR
Demonstrated on a 700 TPD chlor-alkali case
120 consecutive delivery days, replayed at settled prices, against the plant's real counterfactual: one steady setpoint per asset held all day.
₹0.133
net saving per kWh of total plant load, with real forecast error
₹9.17 cr
annualised · 1.53% of the bill
0
violations · 0 MW deviation used
13 / 120
days worse than doing nothing
PRANA does not manufacture savings. When flexibility is not worthwhile it can lose: a single-asset site with a hard production floor has no second lever when the forecast is wrong. The 13 days are reported, not removed.
GROSS TO NET, ₹ LAKH OVER 120 DAYS
378.3
Gross benefit
−76.8
Process costs
301.5
Net benefit
Process cost is membrane wear, chlorine diverted to bleach, and kVAh droop one fifth of the gross, paid straight back. A model that does not charge these is not conservative, it is wrong.
120 delivery days to 2026-08-06, settled at realised prices. Perfect foresight would be ₹0.174/kWh; the forecast-error haircut is 22%. Figures are for this demonstrator plant, not a sector claim.
Notes: Label it out loud as a demonstrator, not a product line. 120 consecutive delivery days, replayed at settled prices, against the counterfactual of one steady setpoint per asset held all day — which is how the plant is actually run. Quote the forecast-error figure, never perfect foresight: ₹0.133 per kWh net. Then go straight at the 13 out of 120. PRANA does not manufacture savings; when flexibility is not worthwhile it can lose, and a single-asset site with a hard 70% floor has no second lever when the forecast is wrong. That is the honest argument for adding a second flexible asset, not for hiding the row. Q: What happens when the forecast is wrong? The optimiser carries a CVaR risk term and a quantile fan rather than a point forecast, and the haircut against perfect foresight is 22% — reported, not removed.

## Slide 10
SCALE, AND THE ASK
10 / 10
One demonstrator. A platform for industrial flexibility.
Chlor-alkali
DEMONSTRATED · 120 DAYS
Refinery
NEXT VALIDATION TARGET
Chemicals
VALIDATION TARGET
Fertilizer
VALIDATION TARGET
Hydrogen
DEPLOYMENT TARGET
No savings are claimed for any unvalidated industry. Each one earns its number the same way chlor-alkali did.
90-DAY ADVISORY PILOT
Weeks 1–4
Plant-specific digital twin, fitted to their historian
Weeks 5–8
Flexibility cost curve φ the number they have never had
Weeks 9–12
Shadow-mode optimisation, compared against actuals daily
Lower landed electricity cost
Zero product-spec excursions
Zero safety violations
No production authority transferred
PRANA does not tell the plant what equipment to sacrifice. It tells the plant what flexibility it can safely afford.
Notes: Be disciplined here: one demonstrated case, everything else marked as a validation target with no savings attached to it. Then the ask — ninety days, advisory only, one plant. Weeks 1–4 build the plant-specific twin; weeks 5–8 deliver φ, the number they have never had about their own process; weeks 9–12 shadow mode, a recommended profile each morning compared against actuals each evening at realised prices. Success is agreed up front and includes zero excursions and zero safety violations, and no production authority changes hands. Q: How would this work in a refinery? Same five stages, different physics — compressor maps and intermediate tankage instead of a cell curve and a caustic tank. Close on the final line and stop talking.